## Slide 1: Interferometry Celebration
Spokane Astronomical Society
May 2, 2003

## Slide 2: History
Notes: Young – 1803 Bakerian Lectures, Michelson 1882, 1907, 1920 “Differential Refractometer”. Ryle Vonberg 1947 MRAO Cambridge. Hanbury-Twiss, Brown 1957. Antoine Labeyrie 1975.

## Slide 3: Keck
Notes: CARA, 2 elements, (4 more planned), Main elements are 10 meter but the satellites will only be 1.8 meter mirrors. The baseline is 140 meters. June 2002

## Slide 5: COAST
Notes: COAST Cambridge Optical Aperture Synthesis Telescope, MRAO England FF 95 on Capella twins. 5 elements (40cm ea), 22 meter baseline

## Slide 6: NPOI
Notes: NPOI Navy Prototype Optical Interferometer, Lowell Observatory, Anderson Mesa, Arizona
6 elements (60cm ea), 145m baseline. First synthetic image in March 1996

## Slide 7: IOTA
Notes: Cfa/U Mass, Mount Hopkins 3 elements (45cm ea), 38 m baseline. First Synthetic image in February 2002 after it got IONIC 3-way combiner.

## Slide 8: PTI
Notes: PTI Palomar testbed interferometer, Mount Palomar, California
2 elements ( 40cm ea), 110 m baseline. NICMOS combiner.

## Slide 9: CHARA
Notes: Georgia State Univ., Mount Wilson
6 elements (10 cm ea.), 350 m baseline. FF November 1999. FLUOR fiber-optic combiner since Augusst 2002.

## Slide 10: SUSI
Notes: SUSI Sydney University Stellar Interferometer. Narrabri Australia
13 elements (14cm ea), 640 m baseline

## Slide 11: MIRA

## Slide 12: VLTI
Notes: Cerra Paranal. FF October 29, 2001 with VINCI fiber-optic combiner. MIDI combiner installed in December 2002.

## Slide 14: Fringe Visibility
Constructive & destructive interference of light
Fringe contrast or visibility:
Calibration issues
  Detector linearity
  Zero point measm’t
  Noise characterizat’n
I+
I-
Noise
Actual starlight fringes from IOTA -  And
Photo credit: R.R. Thompson
Zero
OPD
Fringe
Envelope
Notes: 2. A good basic "fringe" picture, showing starlight intensity on a time-lapse photo
of an oscilliscope as the zero path position was swept through at IOTA. I spent
*many* (300+) nights at IOTA staring at the 'scope, looking for fringes packets just
like this one...

## Slide 15
Initial Indications of Something Interesting with Altair
Use of the PTI N-S and N-W baselines gave different angular sizes
Not explainable in terms of limb darkening, spotting, binarity
N-W Baseline
N-S Baseline
50°

## Slide 16
Notes: Gerard’s JPL presentation on Altair

## Slide 17: Modes and Uses
Astrometry
Planets Angular Diameter – Rotation
Hot Jupiters
Nulling
Circumstellar dust
Planets
Imaging
Protoplanetary disks
Two-color differential Astrometry
Venus-sized planets
Notes: Nulling: Reject light from central star
Two-color differential astrometry
Astrometry
Differential astrometry
Imaging

## Slide 18: LIGO

## Slide 21
Notes: Crab Nebula (M1) in Taurus. X-ray and Infrared. Pulsar 30 rps.

## Slide 25
-- GEO
-- L 2km
-- H 4km
-- L 4km
Crab pulsar
hc
S1 sensitivities

## Slide 29: Radio

## Slide 30: Sub millimeter Array on Mauna Kea

## Slide 31: M33 doppler in Radio